Lightning Generator v1.5
(Unity 5.4.1)

Mini Manual

     www.kerkero.ru 2016

______________________________________________

Lighting Box

“Lighting Box” - main prefab. Drag it to the scene.

Main settings

:Size:

Coordinates corresponding to the size of the object, which will spawn lightning.

:Auto Spawn:
If true, then the lightning will spawn.

Min/Max delay before the spawn of the next lightning.

After each spawn, delay is calculated randomly
relative to the minimum and maximum.
______________________________________________

Additional settings

Click Lighting Prefab

:Sound:

Delay sound of thunder calculated the relative distance to the Main Camera.

:Rods:

1. "Use Rod" - lightning will sometimes strike the rod.

2. "Force Use Rod" ("Use Rod" should be enabled) - lightning will always strike the rod.

3.To the object became a lightning rod, you need to add a script : "LightningRod"

:Max height lightning:

Height in units is shown in "Lightning Box"

______________________________________________